## Slide 1: Semiconductor Industry, Business Models & IC Lifecycle
Week – 1 Day – 1

## Slide 2: Semiconductor Testing Engineering
Semiconductor Industry, Business Models & IC Lifecycle
From IC Idea → Design → Manufacturing → Testing → Product

## Slide 3: Today's Learning Objectives
By the end of today's class, learners will be able to:
Explain the semiconductor industry ecosystem
Describe the semiconductor value chain
Differentiate:
  Fabless
  Foundry
  IDM
  OSAT
Explain the IC lifecycle
Identify major semiconductor testing stages
Identify key roles in semiconductor testing
Explain how engineering decisions affect testing

## Slide 4: Why Should a Test Engineer Understand the Industry?
A semiconductor test engineer works within a larger ecosystem:
Design → Wafer Fabrication → Wafer Sort → Assembly → Package Test → Final Test → Qualification → Shipment
Testing decisions affect:
Product quality
Yield
Cost
Reliability
Production time
Customer satisfaction

## Slide 5: What Is a Semiconductor?
A semiconductor is a material whose electrical conductivity can be controlled.
Common semiconductor materials:
Silicon
Germanium
Gallium nitride
Silicon carbide
Semiconductors are used to build:
Diodes
Transistors
Integrated circuits
Sensors
Power devices
Microprocessors
Memories

## Slide 6: What Is an Integrated Circuit?
Integrated Circuit (IC)
A semiconductor device containing many interconnected electronic components on a small piece of semiconductor material.
Examples:
Microcontroller
CPU
GPU
Memory
ADC
DAC
Power management IC
Communication IC
Sensor IC

## Slide 7: The Semiconductor Industry Ecosystem
SEMICONDUCTOR INDUSTRY
┌───────────────┐
│ IC DESIGN │
└───────┬───────┘
↓
┌───────────────┐
│ WAFER FAB │
└───────┬───────┘
↓
┌───────────────┐
│ WAFER SORT │
└───────┬───────┘
↓
┌───────────────┐
│ ASSEMBLY │
└───────┬───────┘
↓
┌───────────────┐
│ FINAL TEST │
└───────┬───────┘
↓
┌───────────────┐
│ QUALIFICATION │
└───────┬───────┘
↓
CUSTOMER

## Slide 8: Semiconductor Value Chain
Stage | Main Activity
Specification | Define product requirements
Architecture | Define system structure
Design | Create circuits/layout
Fabrication | Build devices on wafer
Wafer Sort | Test individual dies
Assembly | Package the die
Final Test | Test packaged IC
Qualification | Verify long-term performance
Shipment | Deliver qualified products

## Slide 9: Four Major Semiconductor Business Models
1. Fabless
Designs ICs but generally does not operate its own wafer fabrication facility.
2. Foundry
Manufactures wafers for customers.
3. IDM
Integrated Device Manufacturer — designs and manufactures semiconductor products within an integrated business.
4. OSAT
Outsourced Semiconductor Assembly and Test provider.

## Slide 10: Fabless Model
Fabless = Design-focused company
Typical responsibilities:
Product definition
Architecture
Circuit design
Verification
Physical design
Design-for-Test
Test development
Product engineering
Manufacturing is outsourced.

## Slide 11: Foundry Model
Foundry = Manufacturing-focused company
Customer provides:
Design
Layout
Manufacturing requirements
Foundry provides:
Wafer fabrication
Process technology
Manufacturing infrastructure
Process control

## Slide 12: IDM Model
IDM — Integrated Device Manufacturer
One organization can control major portions of:
Design → Fabrication → Assembly → Test
Advantages:
Greater control
Internal process knowledge
Close integration
Challenges:
Very high capital investment
Complex manufacturing infrastructure

## Slide 13: OSAT Model
OSAT = Outsourced Semiconductor Assembly and Test
Typical responsibilities:
Package assembly
Package-related processes
Electrical testing
Final testing
Handling
Inspection
OSAT companies provide manufacturing services to semiconductor companies.

## Slide 14: Business Model Comparison
Model | Design | Fab | Assembly | Test
Fabless | ✓ | Outsourced | Outsourced | Outsourced / Partner
Foundry | Customer | ✓ | Usually external | Usually external
IDM | ✓ | ✓ | ✓ / Integrated | ✓
OSAT | Customer | — | ✓ | ✓

## Slide 15: Classroom Activity: Identify the Business Model
Scenario
Company A:
Designs smartphone processors
Does not operate a wafer fab
Sends wafer designs to a manufacturing partner
What business model?
A. IDM B. Foundry C. Fabless D. OSAT

## Slide 16: What Is the IC Lifecycle?
Product Idea
↓
Specification
↓
Architecture
↓
Design
↓
Verification
↓
Tape-out
↓
Wafer Fabrication
↓
Wafer Sort
↓
Assembly / Packaging
↓
Final Test
↓
Qualification
↓
Production
↓
Shipment

## Slide 17: Product Specification
Before designing an IC, engineers define:
Function
Performance
Power consumption
Operating voltage
Operating temperature
Speed
Interfaces
Package
Reliability requirements
Cost target

## Slide 18: IC Architecture & Design
Architecture
Defines:
Functional blocks
Data paths
Interfaces
Memory
Clocking
Power domains
Design
Converts architecture into:
Schematics
RTL
Logic
Physical layout
Mask data

## Slide 19: Verification vs Testing
Design Verification
"Did we design the IC correctly?"
Manufacturing Test
"Did we manufacture the IC correctly?"
Qualification
"Will the product continue to meet requirements under defined conditions?"

## Slide 20: Tape-Out
Tape-out
The finalized design data is released for manufacturing.
After tape-out:
Design → Manufacturing
Typical transition:
Electronic Design
↓
Physical Layout
↓
Design Verification
↓
Tape-out
↓
Mask / Manufacturing Data
↓
Wafer Fabrication

## Slide 21: Where Does Test Engineering Enter?
Test engineering interacts with multiple stages:
Product specification
Design
DFT
Wafer sort
Package test
Final test
Qualification
Production
Yield analysis
Failure analysis

## Slide 22: What Is DFT?
DFT = Design for Testability
Design techniques that make an IC easier to test.
Examples:
Scan chains
ATPG
JTAG
Boundary scan
MBIST
Test modes

## Slide 23: Major Test Stages
Characterization
Understand device behavior.
Validation
Confirm product meets design/specification requirements.
Production Test
Screen manufactured devices at scale.
Reliability Test
Evaluate behavior under defined stress conditions.
These testing stages are included in the competency range.

## Slide 24: Wafer Sort vs Final Test
Wafer Sort | Final Test
Die is still on wafer | Packaged device
Tests individual dies | Tests packaged IC
Helps identify bad dies | Screens finished products
Before packaging | After packaging

## Slide 25: Why Testing Is a Business Requirement
Testing helps control:
Quality
Yield
Cost
Reliability
Customer Risk
Production Efficiency

## Slide 26: Test Engineer Roles
Possible semiconductor testing roles:
Test Engineer
ATE Test Engineer
Product Engineer
Test Development Engineer
IC Test Engineer
Yield Engineer
Failure Analysis Support Engineer
These roles are identified in the competency standard.

## Slide 27: What Does a Test Engineer Do?
Typical responsibilities:
Develop test strategy
Develop test programs
Define test conditions
Debug failures
Analyze test data
Optimize test time
Improve yield
Support production
Investigate failures
Document results

## Slide 28: Career Path
Trainee / Junior Engineer
↓
Test Engineer
↓
Senior Test Engineer
↓
Lead / Principal Engineer
↓
Technical Specialist / Manager
Possible specialization:
ATE
Test Hardware
Product Engineering
Yield
DFT
Analog/Mixed Signal
Failure Analysis

## Slide 29: Activity: Map the Lifecycle
Arrange the following in the correct order:
Final Test
Design
Wafer Sort
Specification
Assembly
Fabrication
Qualification
Shipment

## Slide 30: Knowledge Check
What is a fabless company?
What does OSAT mean?
What is an IDM?
What is wafer sort?
What is final test?
Why is DFT important?
Name three semiconductor test roles.

## Slide 31: Day 1 Summary
Remember:
Semiconductor ecosystem
→ Design
→ Manufacturing
→ Assembly
→ Test
→ Qualification
→ Customer
Four business models
Fabless | Foundry | IDM | OSAT
Test Engineering
Quality + Yield + Cost + Reliability + Production