## Slide 1: Wafer Fabrication, Assembly, Packaging & Test Flow
Week – 1
Day – 2

## Slide 2: Semiconductor Testing Engineering
Wafer Fabrication, Assembly, Packaging & Test Flow
From Silicon Wafer → Packaged IC → Tested Product

## Slide 3: Learning Objectives
By the end of today's class, learners will be able to:
Explain the overall semiconductor manufacturing flow
Describe major wafer fabrication steps
Explain wafer preparation
Explain oxidation, deposition and lithography
Describe etching and implantation
Explain metallization
Explain wafer probing / wafer sort
Describe assembly and packaging
Differentiate package test and final test
Explain the interface between package and test hardware

## Slide 4: Complete Semiconductor Manufacturing Flow
Silicon
↓
Wafer Manufacturing
↓
Wafer Fabrication
↓
Wafer Electrical Test / Wafer Sort
↓
Die Separation
↓
Assembly
↓
Packaging
↓
Package / Final Test
↓
Qualification
↓
Shipment

## Slide 5: What Is a Wafer?
A wafer is a thin, flat semiconductor substrate used to manufacture multiple IC dies.
Each small section represents a potential die.

## Slide 6: Wafer → Die → Package
WAFER
↓
Individual DIE
↓
PACKAGED IC
↓
TESTED IC

## Slide 7: What Happens During Wafer Fabrication?
Wafer fabrication creates microscopic electronic structures through repeated processes.
Major process categories:
Cleaning
Oxidation
Deposition
Photolithography
Etching
Ion implantation
Metallization
Planarization
Inspection / measurement

## Slide 8: Starting Silicon
Silicon Manufacturing
Silicon source
↓
High-purity silicon
↓
Crystal growth
↓
Ingot
↓
Slicing
↓
Polishing
↓
Silicon wafer

## Slide 9: Wafer Cleaning
Why Clean the Wafer?
Contamination can cause:
Defects
Electrical failures
Yield loss
Reliability problems
Cleaning removes unwanted:
Particles
Organic contamination
Metallic contamination
Native surface contamination

## Slide 10: Oxidation
Oxidation
Forms a controlled oxide layer on the silicon surface.
Simplified:
Silicon Surface
───────────────
↓ oxidation
Oxide Layer
═══════════════
Silicon
───────────────

## Slide 11: Deposition
Deposition
Adds a thin material layer to the wafer.
Possible deposited materials include:
Dielectrics
Conductive materials
Semiconductor materials
Concept:
Existing Layer
──────────────
New Layer
══════════════

## Slide 12: Photolithography
Purpose
Transfers a pattern onto the wafer.
Simplified flow:
Photoresist
↓
Mask / Pattern
↓
Exposure
↓
Development
↓
Patterned Surface

## Slide 13: Etching
Etching = selective removal of material
Before
████████████████
████████████████
████████████████
After patterning/etching
██████ ██████
██████ ██████
██████ ██████

## Slide 14: Ion Implantation
Ion Implantation
Introduces controlled dopant atoms into semiconductor material.
Purpose:
Modify electrical properties
Create semiconductor regions
Form device structures
Concept:
Ion beam
↓↓↓↓↓↓↓↓
────────────
Silicon
────────────

## Slide 15: Metallization
Creates conductive interconnections between circuit elements.
Device A ───────── Device B
Metal
Purpose:
Electrical connectivity
Signal routing
Power distribution

## Slide 16: Planarization / CMP
CMP — Chemical Mechanical Planarization
Purpose:
Make the wafer surface sufficiently flat for subsequent processing.
Uneven Surface
^^^^^^^^^^^^^^
↓
Flat Surface
──────────────

## Slide 17: Repeated Manufacturing Layers
Modern IC fabrication is a repetitive layered process.
Layer N
════════════
Layer N-1
────────────
Layer N-2
════════════
Layer N-3
────────────
Silicon
████████████

## Slide 18: From Wafer Fabrication to Completed Wafer
Raw Wafer
↓
Process Layers
↓
Device Structures
↓
Interconnects
↓
Passivation
↓
Completed IC Wafer

## Slide 19: Wafer Sort
Wafer Sort
Electrical testing is performed while dies are still on the wafer.
Purpose:
Identify good dies
Identify failing dies
Measure electrical parameters
Support yield analysis
Prevent bad dies from progressing unnecessarily

## Slide 20: Probe Card
TESTER
│
Probe Card
│
↓ ↓ ↓ ↓ ↓
┌─────────────┐
│ WAFER │
│ □ □ □ □ □ □ │
│ □ □ □ □ □ □ │
└─────────────┘

## Slide 21: Wafer Sort Data
A wafer map can show:
Pass dies
Fail dies
Parametric results
Spatial patterns
Example:
WAFER MAP
✓ ✓ ✓ ✗ ✓ ✓
✓ ✓ ✓ ✓ ✓ ✓
✓ ✗ ✓ ✓ ✓ ✓
✓ ✓ ✓ ✓ ✗ ✓

## Slide 22: Die Separation
After wafer testing:
Wafer → Individual Dies
Typical concept:
Completed Wafer
↓
Die Separation
↓
Individual Dies

## Slide 23: Semiconductor Assembly
Basic assembly concept:
Good Die
↓
Die Attach
↓
Electrical Interconnection
↓
Encapsulation / Package Formation
↓
Package Marking
↓
Packaged IC

## Slide 24: Why Do We Need Packaging?
Packaging provides:
Protection
Protects the die from the environment.
Electrical Connection
Connects internal die circuitry to external pins/balls.
Mechanical Support
Allows the device to be handled and mounted.
Thermal Management
Helps manage heat.

## Slide 25: Package Types
Examples:
DIP
SOIC
QFP
QFN
BGA
CSP
WLCSP
Package selection affects:
Pin count
Size
Thermal performance
Electrical performance
Assembly
Test interface

## Slide 26: Package Electrical Interface
Inside the package:
DIE
┌────────────┐
│ │
│ IC CIRCUIT │
│ │
└────────────┘
│ │ │
│ │ │
Electrical
connections
│ │ │
↓ ↓ ↓
Package Pins

## Slide 27: Package Test vs Final Test
Depending on the manufacturing organization/product terminology, testing may include:
Package Test
Testing after packaging.
Final Test
Testing packaged devices before release/shipment.
Typical checks can include:
Functional behavior
DC parameters
AC parameters
Leakage
Voltage/current
Timing
Performance

## Slide 28: Complete Test Flow
IC LIFECYCLE
Design
↓
Fabrication
↓
Wafer Sort
↓
Assembly
↓
Package Test
↓
Final Test
↓
Qualification
↓
Shipment

## Slide 29: Test Hardware Interface
ATE
│
↓
Loadboard
│
↓
Socket
│
↓
Packaged IC
│
↓
DIE

## Slide 30: Practical Activity: Identify the Stage
Match each activity to the correct stage:
A. Wafer Sort B. Assembly C. Final Test D. Fabrication
Photolithography
Electrical testing of individual dies
Die attach
Functional testing of packaged IC

## Slide 31: Final Knowledge Check
Questions
What is a wafer?
What is a die?
Why is photolithography used?
What is deposition?
What is etching?
Why is ion implantation used?
What is wafer sort?
Why is packaging necessary?
What is the difference between wafer sort and final test?
What is the purpose of a loadboard?

## Slide 32: Day 2 Summary
Remember the Flow
Silicon
↓
Wafer Fabrication
↓
Wafer Sort
↓
Die Separation
↓
Assembly
↓
Packaging
↓
Final / Package Test
↓
Qualification
↓
Shipment

## Slide 33: Preview of Day 3
Tomorrow
Electronics & Semiconductor Device Fundamentals
We will study:
Basic circuit quantities
Semiconductor concepts
Diodes
Transistors
MOS devices
Operating regions
Device behavior