## Slide 1
SEMICONDUCTOR TESTING ENGINEERING · WEEK 1 — DAY 1
Semiconductor Industry, Business Models & IC Lifecycle
From IC Idea → Design → Manufacturing → Testing → Product
ITEST BANGLADESH · TRAINING PROGRAM
▿
Si

## Slide 2
COURSE OVERVIEW
Semiconductor Testing Engineering
Semiconductor Industry, Business Models & IC Lifecycle
IC Idea
→
Design
→
Manufacturing
→
Testing
→
Product
INDUSTRY
▿
BUSINESS MODELS
✿
IC LIFECYCLE
↻
TEST STAGES
✓
ITEST BANGLADESH · WEEK 1 · DAY 1
02 / 35

## Slide 3
TODAY'S CLASS
Learning Objectives
By the end of today's class, learners will be able to:
01
Explain the semiconductor industry ecosystem
02
Describe the semiconductor value chain
03
Differentiate: Fabless · Foundry · IDM · OSAT
04
Explain the IC lifecycle
05
Identify major semiconductor testing stages
06
Identify key roles in semiconductor testing
07
Explain how engineering decisions affect testing
08
Connect business model choices to test strategy
ITEST BANGLADESH · WEEK 1 · DAY 1
03 / 35

## Slide 4
CONTEXT
Why Should a Test Engineer Understand the Industry?
A TEST ENGINEER WORKS WITHIN A LARGER ECOSYSTEM
Design
→
Wafer Fabrication
→
Wafer Sort
→
Assembly
→
Package Test
→
Final Test
→
Qualification
→
Shipment
TESTING DECISIONS AFFECT
A test engineer's choices ripple through every downstream metric the business cares about — from yield to customer trust.
✓
Product Quality
↗
Yield
$
Cost
⛨
Reliability
◔
Production Time
☻
Customer Satisfaction
ITEST BANGLADESH · WEEK 1 · DAY 1
04 / 35

## Slide 5
CHAPTER 01 OF 04
01
Foundations
What semiconductors and integrated circuits actually are — the vocabulary every test engineer needs before anything else makes sense.
What Is a Semiconductor?
What Is an Integrated Circuit?
The Industry Ecosystem
The Semiconductor Value Chain

## Slide 6
FOUNDATIONS · 01
What Is a Semiconductor?
A semiconductor is a material whose electrical conductivity can be controlled — the foundation of every modern electronic device.
COMMON MATERIALS
⚗
▦
Silicon (Si)
☂
Germanium (Ge)
⚡
Gallium Nitride (GaN)
◆
Silicon Carbide (SiC)
BUILT FROM SEMICONDUCTORS
⚒
Diodes
Transistors
Integrated Circuits
Sensors
Power Devices
Microprocessors
Memories
ITEST BANGLADESH · WEEK 1 · DAY 1
06 / 35

## Slide 7
FOUNDATIONS · 02
What Is an Integrated Circuit?
DEFINITION
Integrated Circuit (IC)
A semiconductor device containing many interconnected electronic components on a small piece of semiconductor material.
COMPONENTS
▦
Billions
SIZE
✦
mm-scale
LAYERS
✦
10s+
EXAMPLE IC TYPES
✦
Microcontroller
▢
CPU
▶
GPU
▦
Memory
▦
ADC
⚙
DAC
⚡
Power Management IC
✦
Sensor IC
ITEST BANGLADESH · WEEK 1 · DAY 1
07 / 35

## Slide 8
FOUNDATIONS · 03
The Semiconductor Industry Ecosystem
A linear flow of value — from design idea to qualified customer shipment.
◆
IC DESIGN
◔
WAFER FAB
✓
WAFER SORT
▣
ASSEMBLY
⚗
FINAL TEST
⛨
QUALIFICATION
⊟
SHIPMENT
☻
CUSTOMER
Each stage adds value — and each stage introduces potential defects that test engineering must catch.
ⓘ
ITEST BANGLADESH · WEEK 1 · DAY 1
08 / 35
›
›
›
›
›
›
›

## Slide 9
FOUNDATIONS · 04
Semiconductor Value Chain
Nine stages, each with a distinct engineering responsibility.
Stage | Main Activity
01Specification | Define product requirements
02Architecture | Define system structure
03Design | Create circuits/layout
04Fabrication | Build devices on wafer
05Wafer Sort | Test individual dies
06Assembly | Package the die
07Final Test | Test packaged IC
08Qualification | Verify long-term performance
09Shipment | Deliver qualified products
ITEST BANGLADESH · WEEK 1 · DAY 1
09 / 35

## Slide 10
CHAPTER 02 OF 04
02
Business Models
Four ways the industry organizes itself — and how each one shapes where testing work actually happens.
Fabless · Design-led
Foundry · Manufacturing-led
IDM · Vertically Integrated
OSAT · Assembly & Test Partner

## Slide 11
BUSINESS MODELS · OVERVIEW
Four Major Semiconductor Business Models
Each model decides who designs, who builds, who tests — and where the engineering work lives.
01
❄
Fabless
DESIGN-FOCUSED COMPANY
Designs ICs but generally does not operate its own wafer fabrication facility. Manufacturing is outsourced to a foundry partner.
02
◔
Foundry
MANUFACTURING-FOCUSED COMPANY
Manufactures wafers for customers. Provides process technology, infrastructure, and process control.
03
✦
IDM
INTEGRATED DEVICE MANUFACTURER
Designs and manufactures semiconductor products within a single integrated business. End-to-end control.
04
✻
OSAT
OUTSOURCED ASSEMBLY & TEST
Outsourced Semiconductor Assembly and Test provider. Handles packaging, electrical testing, final test.
ITEST BANGLADESH · WEEK 1 · DAY 1
11 / 35

## Slide 12
BUSINESS MODELS
01
FABLESS
02
FOUNDRY
03
IDM
04
OSAT
Each model places test engineering work in a different organization.
BUSINESS MODELS · 01
Fabless Model
Fabless = Design-focused company
TYPICAL RESPONSIBILITIES
Product Definition
Architecture
Circuit Design
Verification
Physical Design
Design-for-Test
Test Development
Product Engineering
Manufacturing is outsourced — typically to a foundry partner.
☎
ITEST BANGLADESH · WEEK 1 · DAY 1
12 / 35

## Slide 13
BUSINESS MODELS
01
FABLESS
02
FOUNDRY
03
IDM
04
OSAT
Each model places test engineering work in a different organization.
BUSINESS MODELS · 02
Foundry Model
Foundry = Manufacturing-focused company
CUSTOMER PROVIDES
☻
FOUNDRY PROVIDES
✦
❄
Design
▦
Layout
▤
Manufacturing requirements
◔
Wafer fabrication
▦
Process technology
▥
Manufacturing infrastructure
⚙
Process control
ⓘ
A foundry never designs the chip — it builds someone else's design on its process.
ITEST BANGLADESH · WEEK 1 · DAY 1
13 / 35

## Slide 14
BUSINESS MODELS
01
FABLESS
02
FOUNDRY
03
IDM
04
OSAT
Each model places test engineering work in a different organization.
BUSINESS MODELS · 03
IDM Model
IDM — Integrated Device Manufacturer
One organization can control major portions of the entire semiconductor value chain — from design through final test.
DESIGN
✓
›
FABRICATION
✓
›
ASSEMBLY
✓
›
TEST
✓
ADVANTAGES
👍
Greater control over the entire product
Internal process knowledge and IP
Close integration across stages
CHALLENGES
⚠
Very high capital investment
Complex manufacturing infrastructure to maintain
ITEST BANGLADESH · WEEK 1 · DAY 1
14 / 35

## Slide 15
BUSINESS MODELS
01
FABLESS
02
FOUNDRY
03
IDM
04
OSAT
Each model places test engineering work in a different organization.
BUSINESS MODELS · 04
OSAT Model
OSAT = Outsourced Semiconductor Assembly and Test
TYPICAL RESPONSIBILITIES
▣
Package Assembly
Die attach, wire bonding, molding
◔
Package Processes
Trim, form, singulation
⚡
Electrical Testing
Open/short, parametric checks
✓
Final Testing
Full-speed production test
⚒
Handling
Tape & reel, tray packing
⌕
Inspection
Visual + AOI quality checks
▭
OSAT companies provide manufacturing services to semiconductor companies — they don't design the chip themselves.
ITEST BANGLADESH · WEEK 1 · DAY 1
15 / 35

## Slide 16
BUSINESS MODELS · COMPARISON
Business Model Comparison
Who does what — at a glance.
Model | Design | Fab | Assembly | Test
Fabless | ✓Outsourced | Outsourced | Outsourced | Outsourced / Partner
Foundry | Customer | ✓ | Usually external | Usually external
IDM | ✓ | ✓ | ✓Integrated | ✓
OSAT | Customer | — | ✓ | ✓
ⓘ
No single model is universally best — the right choice depends on the product, volume, IP strategy, and capital position.
ITEST BANGLADESH · WEEK 1 · DAY 1
16 / 35

## Slide 17
CLASSROOM ACTIVITY · 01
Identify the Business Model
SCENARIO
◆
Company A
◖
Designs smartphone processors
◖
Does not operate a wafer fab
◖
Sends wafer designs to a manufacturing partner
WHAT BUSINESS MODEL?
✦
A
IDM
B
Foundry
C
Fabless
D
OSAT
◆
Hint: think about who owns the design vs. who runs the fab.
ITEST BANGLADESH · WEEK 1 · DAY 1
17 / 35

## Slide 18
CHAPTER 03 OF 04
03
IC Lifecycle
From product idea to shipment — the 13 stages every integrated circuit passes through before it reaches a customer.
IN THIS CHAPTER
01
Product Specification
→
02
Architecture & Design
→
03
Verification vs Testing
→
04
Tape-Out
→

## Slide 19
IC LIFECYCLE · OVERVIEW
What Is the IC Lifecycle?
Thirteen stages from idea to shipment.
01
PRODUCT IDEA
02
SPECIFICATION
03
ARCHITECTURE
04
DESIGN
05
VERIFICATION
06
TAPE-OUT
07
WAFER FABRICATION
→
13
SHIPMENT
12
PRODUCTION
11
QUALIFICATION
10
FINAL TEST
09
ASSEMBLY / PACKAGING
08
WAFER SORT
✦
Each stage is a handoff — and each handoff is a chance for defects to enter or be caught.
ITEST BANGLADESH · WEEK 1 · DAY 1
19 / 35

## Slide 20
IC LIFECYCLE · 01
Product Specification
Before designing an IC, engineers define the requirements the product must meet.
⚑
Function
What it does
✦
Performance
How fast / well
⚡
Power
Consumption budget
⚡
Voltage
Operating range
✦
Temperature
Operating range
▦
Speed
Clock targets
✦
Interfaces
I/O standards
▣
Package
Physical form
⛨
Reliability
Lifetime goals
$
Cost
Unit cost target
!
A vague specification is the single most expensive defect in the entire lifecycle.
ITEST BANGLADESH · WEEK 1 · DAY 1
20 / 35

## Slide 21
IC LIFECYCLE · 02
IC Architecture & Design
Architecture defines what the chip does. Design turns that definition into something that can actually be built.
✿
ARCHITECTURE
DEFINES:
Functional Blocks
Data Paths
Interfaces
Memory
Clocking
Power Domains
❄
DESIGN
CONVERTS ARCHITECTURE INTO:
Schematics
RTL
Logic
Physical Layout
Mask Data
⋯
ⓘ
A clean architecture makes the design phase tractable. A messy architecture makes every downstream stage harder.
ITEST BANGLADESH · WEEK 1 · DAY 1
21 / 35
→

## Slide 22
IC LIFECYCLE · 03
Verification vs Testing
Three questions engineers ask at three different points in the lifecycle.
▣
Design Verification
PRE-SILICON
"Did we design the IC correctly?"
Happens before tape-out, using simulation, formal methods, and emulation on the RTL model.
✓
Manufacturing Test
POST-SILICON
"Did we manufacture the IC correctly?"
Happens after fabrication, using ATE test programs at wafer sort and final test.
⛨
Qualification
LONG-TERM
"Will the product continue to meet requirements under defined conditions?"
Happens on a sample basis, using accelerated stress testing (HTOL, HAST, temp cycle, ESD).
ITEST BANGLADESH · WEEK 1 · DAY 1
22 / 35

## Slide 23
IC LIFECYCLE · 04
Tape-Out
DEFINITION
⚑
Tape-out
The finalized design data is released for manufacturing — the handoff from design world to fab world.
→
After tape-out: Design → Manufacturing
TYPICAL TRANSITION
ITEST BANGLADESH · WEEK 1 · DAY 1
23 / 35
01
Electronic Design
✎
02
Physical Layout
▦
03
Design Verification
▣
04
Tape-out
⚑
05
Mask / Manufacturing Data
✦
06
Wafer Fabrication
◔

## Slide 24
CHAPTER 04 OF 04
04
Test Engineering & Career
Where test engineering actually enters the lifecycle — the tools, stages, and career paths that define the profession.
01
Where Test Engineering Enters
02
DFT & Major Test Stages
03
Wafer Sort vs Final Test
04
Roles, Responsibilities & Career Path

## Slide 25
TEST ENGINEERING · TOUCHPOINTS
Where Does Test Engineering Enter?
Test engineering isn't a single stage — it touches almost every point of the IC lifecycle.
01
▤
PRODUCT SPEC
02
❄
DESIGN
03
✦
DFT
04
✓
WAFER SORT
05
▣
PACKAGE TEST
06
⚗
FINAL TEST
07
⛨
QUALIFICATION
08
◔
PRODUCTION
09
↗
YIELD ANALYSIS
10
⌕
FAILURE ANALYSIS
✦
The earlier test engineering enters, the cheaper it is to catch a defect.
ITEST BANGLADESH · WEEK 1 · DAY 1
25 / 35

## Slide 26
TEST ENGINEERING · DFT
What Is DFT?
DFT
✦
Design for Testability
Design techniques that make an IC easier to test — built into the chip itself, not added afterwards.
COMMON DFT TECHNIQUES
⌘
Scan Chains
Shift test data through flops
⚒
ATPG
Auto test pattern generation
✦
JTAG
Boundary-scan standard
✦
Boundary Scan
Test board-level connections
▦
MBIST
Self-test for embedded memory
⚙
Test Modes
Dedicated test operating modes
ITEST BANGLADESH · WEEK 1 · DAY 1
26 / 35

## Slide 27
TEST ENGINEERING · STAGES
Major Test Stages
Four stages of testing, each answering a different question about the device.
▦
STAGE 01
Characterization
Understand device behavior — explore the envelope across voltage, temperature, and process corners.
▣
STAGE 02
Validation
Confirm the product meets design and specification requirements before production release.
◔
STAGE 03
Production Test
Screen manufactured devices at scale — fast, deterministic, high-throughput.
⛨
STAGE 04
Reliability Test
Evaluate behavior under defined stress conditions — HTOL, HAST, temperature cycle, ESD.
ⓘ
These testing stages are included in the iTest competency range.
ITEST BANGLADESH · WEEK 1 · DAY 1
27 / 35

## Slide 28
TEST ENGINEERING · COMPARISON
Wafer Sort vs Final Test
Two testing gates, two different stages of the device.
◔
Wafer Sort
BEFORE PACKAGING
◖
Die is still on wafer
◖
Tests individual dies
◖
Helps identify bad dies
◖
Before packaging
✓
Final Test
AFTER PACKAGING
◖
Packaged device
◖
Tests packaged IC
◖
Screens finished products
◖
After packaging
⇄
Wafer sort catches defects early and saves packaging cost. Final test guarantees the shipped product meets spec.
ITEST BANGLADESH · WEEK 1 · DAY 1
28 / 35

## Slide 29
TEST ENGINEERING · WHY IT MATTERS
Why Testing Is a Business Requirement
Testing isn't a cost center — it controls six business-critical outcomes simultaneously.
✓
Quality
Defective units never reach the customer
↗
Yield
Maximize the percentage of good dies
$
Cost
Catch defects at the cheapest possible stage
⛨
Reliability
Predict field lifetime and failure modes
⚠
Customer Risk
Limit warranty exposure and recalls
✦
Production Efficiency
Optimize test time per unit
ITEST BANGLADESH · WEEK 1 · DAY 1
29 / 35

## Slide 30
TEST ENGINEERING · ROLES
Test Engineer Roles
Seven distinct roles a semiconductor test engineer can grow into.
⚒
Test Engineer
Generalist across the test lifecycle
▦
ATE Test Engineer
Specializes in automated test equipment
▣
Product Engineer
Owns the product from spec to production
✦
Test Development Engineer
Writes and debugs test programs
▦
IC Test Engineer
Focused on IC-level test strategy
↗
Yield Engineer
Analyzes yield data and defect sources
⌕
Failure Analysis Support Engineer
Investigates failing devices in depth
✓
These roles are identified in the iTest competency standard.
ITEST BANGLADESH · WEEK 1 · DAY 1
30 / 35

## Slide 31
TEST ENGINEERING · RESPONSIBILITIES
What Does a Test Engineer Do?
Ten responsibilities that span the full test engineering lifecycle.
01
Develop test strategy
Define the high-level approach
02
Develop test programs
Write code that runs on the ATE
03
Define test conditions
Set voltages, timings, limits
04
Debug failures
Investigate why a device fails
05
Analyze test data
Find patterns across units and lots
06
Optimize test time
Reduce cost per unit tested
07
Improve yield
Partner with fab and design
08
Support production
Sustain the test floor in volume
09
Investigate failures
Root-cause analysis on field returns
10
Document results
Reports, specs, and learnings
ITEST BANGLADESH · WEEK 1 · DAY 1
31 / 35

## Slide 32
TEST ENGINEERING · CAREER
Career Path
A typical progression — and the specialization tracks that branch off it.
01
Trainee / Junior Engineer
First 1-2 years
02
Test Engineer
Independent contributor
03
Senior Test Engineer
Owns complex programs
04
Lead / Principal Engineer
Sets technical direction
05
Technical Specialist / Manager
Cross-functional leadership
POSSIBLE SPECIALIZATIONS
☎
ATE
Test Hardware
Product Engineering
Yield
DFT
Analog/Mixed Signal
Failure Analysis
↗
Most engineers blend 2-3 of these tracks over time.
ITEST BANGLADESH · WEEK 1 · DAY 1
32 / 35

## Slide 33
CLASSROOM ACTIVITY · 02
Map the Lifecycle
Arrange the following stages in the correct order — from idea to shipment.
STAGE ?
Final Test
STAGE ?
Design
STAGE ?
Wafer Sort
STAGE ?
Specification
STAGE ?
Assembly
STAGE ?
Fabrication
STAGE ?
Qualification
STAGE ?
Shipment
⋮
YOUR TASK
Discuss with your group and arrange the 8 stages in the correct lifecycle order. Be ready to justify your sequence.
5 MIN
◔
ITEST BANGLADESH · WEEK 1 · DAY 1
33 / 35

## Slide 34
CLASSROOM ACTIVITY · 03
Knowledge Check
Quick recall — answer each in one sentence.
Q01
What is a fabless company?
✎
Answer:
Q02
What does OSAT mean?
✎
Answer:
Q03
What is an IDM?
✎
Answer:
Q04
What is wafer sort?
✎
Answer:
Q05
What is final test?
✎
Answer:
Q06
Why is DFT important?
✎
Answer:
Q07
Name three semiconductor test roles.
✎
Answer:
◆
Hint: revisit slides 11, 13, 14, 27, and 30.
ITEST BANGLADESH · WEEK 1 · DAY 1
34 / 35

## Slide 35
WEEK 1 · DAY 1 · COMPLETE
Thank You
Semiconductor Industry, Business Models & IC Lifecycle
Today we covered the ecosystem, the four business models, the IC lifecycle, and where test engineering enters.
NEXT CLASS: WEEK 1 — DAY 2
▦
TOPIC: TEST PROGRAM DEVELOPMENT
▤
QUESTIONS? INFO@ITESTBD.COM
✉
ITEST BANGLADESH · SEMICONDUCTOR TESTING ENGINEERING · 35 / 35